| Hypothesis | Responsibility | Credibility |
| --- | --- | --- |
| The wreck is the Grunion | B Abele | 9 |
| The aft battery hatch was blown open | Galler | ? |
| The sub was not surfacing to use the deck gun | B Abele | 4 |
| The shell from the Kano Maru had some effect on depth control | B Abele | 4 |
| There is hydrodynamic damage to the superstructure | B Abele | 9 |
| There is severe crimping where the bow broke off. | B Abele | 7 |
| About 54 ft of the bow is gone | B Abele | 8 |
| Hydrostatic forces bent the bridge hatch as the boat sank | Fakan | ? |
| The bent bridge hatch caused flooding of the CT before it could implode. | Fakan | ? |
| The air induction piping was pulled apart by implosion of the ER overheads before it reached its own deeper crush depth. | Fakan | ? |
| If measured by final compartment volume and cylindricality vs original volume and cylindricality, the crushing of the ATR appears more severe than any other compartment. | Galler | ? |
| The Aft escape trunk hatch is missing | Galler | ? |

Credibility Ratings

| Credibility | Description |
| --- | --- |
| 1 | Hypothesis that appears possible, but is not supported by any evidence, and is suggested only as something to be considered |
| 2 | Hypothesis that appears possible, and which may be supported by apparent evidence that has not yet been evaluated |
| 3 | Hypothesis that appears possible, and which is supported by multiple evidence that has been partially evaluated |
| 4 | Hypothesis that is supported by general personal experience, or by related evidence, or by similar circumstances involving other submarine casualties |
| 5 | Hypothesis that is supported by specific personal experience, or by specific evidence, or by specific circumstances involving other submarine casualties |
| 6 | As in 5, but by considerable evidence and/or very specific similar circumstances. |
| 7 | Hypothesis based on evidence that has been vetted by the group to some degree. |
| 8 | As in 7, but multiple evidence that is shown to be consistent with the physical laws, and a majority of the group agrees. |
| 9 | As in 7, but vetting is extensive, or the Physics (if applicable) has been verified by more than one independent source, and the agreement is close to unanimous. |